## Slide 1: Pwning IoT via Hardware Attacks
Chase Schultz, Senior Security Consultant cschultz@securityevaluators.com

## Slide 2: About ISE
Analysts
White box
Perspective
Hackers; Cryptographers; RE
Research
Routers; NAS; Healthcare
Customers
Companies with high value assets
Exploits
iPhone; Android; Ford; Exxon; Diebold

## Slide 3: whoami
Chase Schultz
Senior Security Consultant
Independent Security Evaluators
Twitter – @f47h3r_b0
Interests:
  Reverse Engineering, Hardware, SDR, Fuzzing, Embedded Systems, Python & Go

## Slide 4: Agenda
Importance of Hardware Hacking & IoT Research
Scope of Workshop
Hardware Hacking Background
Tools of the Trade
Methodology
Examples
Photo Journal
Hands On!!
Resources / Further Reading
Open it up to attendee’s. What do you want to see?

## Slide 5: Why is this important?
Notes: Talk about the current landscape of IoT… So many new products hitting the streets… Smart Home is here / So many personal devices / … Light Bulbs, Home Appliances, Lighting & Energy Control Systems.

## Slide 6: A Journey of Pwnage
Started getting interested in Hardware Hacking & IoT
Software guy goes to school …
Great way to get access and leverage for further research.
Notes: Need to Add Refrences

## Slide 7: IoT?
IoT is a buzzword (duh) …
  Lots of embedded devices doing all the things …
  Smart Homes
  Medical Devices / Entertainment / Health Fitness / Toys / Sensors etc

## Slide 8: Hardware Hacking
Interfaces
  UART (Universal Asynchronous Receive & Transmit)
  JTAG (Joint Test Action Group) – HW Debug
  SPI (Serial Peripheral Interface)
  I2C (Inter-Integrated Circuit)

## Slide 9
Notes: Piper Night Vision Camera and Home Automation System

## Slide 10: Tools of the Trade

## Slide 18: Hardware Attacks (Methodology)
0) Open the device, void your warranty, and join the exploitation party.
Identify Device, hardware revisions, document hardware components
Research chip datasheets - figure out features
Identify hardware communication interfaces possibilities
Continuity Testing and Electrical Pinout Reversing
Identifying wireline protocol logic (How the hell do I talk to these chips?)
Hardware tools for accessing interfaces
Wiring up to to the board
Device Interrogation
Firmware Reverse Engineering
Vulnerability Research / Exploitation

## Slide 19: Void Some Warranties

## Slide 20: RTFM
Datasheets are your friend!
Notes: 1) MX25L32
2) PIC32MX5

## Slide 21: Identifying HW Interfaces

## Slide 25: Pinout Reversing

## Slide 28
VCC Pin – Steady Voltage (Also chirps)
GND Pin – Metal Piece & Pin
Tx Pin – Fluctuation upon boot
Baudrate

## Slide 29: UART to Root Shells

## Slide 32
JTAG – Joint Test Action Group
  Finding TDI (Test Data In), TDO (Test Data Out), TCK (Test Clock), TMS (Test Mode Select), TRST (Test Reset) optional.
  Hardware Debugging via OpenOCD / GDB
  Jtagulator is awesome for brute-forcing pinout

## Slide 33: Dumping Flash w/ Flashrom

## Slide 34: Resources to Learn
Trainings:
  SexViaHex.com – Software Exploitation Via Hardware Exploitation - Xipiter
  Hands on Hardware Hacking – Joe Grand
Blogs
  http://www.devttys0.com/
  https://dontstuffbeansupyournose.com

## Slide 35: HANDS ON!!
If anyone would like to try wiring up a shikra to a UART interface and playing around with a device.
Presoldered SOHO Routers & Home Automation Hubs

## Slide 37: Accessing Shikra via Screen
screen /dev/cu.usbserial-145 115200
^ ^ ^
cmd device name baudrate

## Slide 38: Your Turn!
Enable yourself as a security researcher.
Initial access for further research.
You can do it too! Its fun!

## Slide 39: Thank You!
DEF CON / @IoTVillage / You!
Contact ISE -- https://securityevaluators.com/
 https://github.com/f47h3r/firmware_collection
 @f47h3r_b0

## Slide 40: Get Involved